## Slide 1
15th IAEE European Conference
A system approach for evaluating clean energy goals and the role of flexibility technologies: the case of France
Manuel Villavicencio
Ph.D. candidate
Université Paris-Dauphine, PSL Research University
LEDa – CGEMP
Vienna 06/09/2017

## Slide 2
Agenda
Context and research questions
1
Definitions and methodology for valuating flexibility technologies
2
3
Findings for the case of France
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
4
Conclusions

## Slide 3
1. Context and research questions
The French Power system by 2015:
EOM, Reserve markets and CRM
Peak load = 93.63 GW
Total energy =541.4 TWh/year
VoLL = 10 000 €/MWh
Annual Lost load < 3 h/year
CO2 cost: 6-8 €/ton
Standards |  | H2020 | H2025 | H2030
VRE shares | > | 27% | - | 40%
Nuclear shares | < | - | 50% | 50%
CO2 cost [€/ton] | = | 20 | 20 | 20
The 2015’s French Energy transition Act: How important is the energy policy shock ?
Loi no 2015-992 of 17 August 2015: “Transition énergétique pour la croissance verte”
Installed capacity
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: It is a nuclear dominated system with some hydro a OCGT => moderate flexibility capabilities

## Slide 4
Net demand variability patterns, an interpretation through Scitovsky’s externalities (1954):
RE_share = 0%
RE_share = 20%
RE_share = 40%
RE_share = 60%
1. Context and research questions
Effect of VRE curtailment
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Max load stays high and variability highly increases

## Slide 5
1. Context and research questions
Power Ramp-rate r, Power p and Energy e
Flexibility metrics in power system operations. Source: Ulbig and Andersson 2013
Operational constraints limiting arbitrage produce differences on the marginal value of electricity
Example: Ramping capabilities
Power plant cycling restrictions:
Ramping constraints
Start-up and shut down technical restrictions
Minimum load
In load range
Reserve capabilities
DSM usage restrictions
Among others
But also, cycling is costly..
(Kumar et al. 2012), (Hentschel et al. 2016)
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: As physical constraints limit arbitrage => the marginal value of electricity varies

## Slide 6
Electricity is:
≠
A homogeneous energy vector
(physics)
A heterogeneous financial good
(economics)
Marginal value space of electricity (heterogeneity). Source: Hirth 2015
1. Context and research questions
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: At a given point in this three-dimensional space, electricity is a perfectly homogenous good.
Electricity is heterogeneous because not all elements of v are the same.
As physical constraints limit arbitrage, the marginal value varies along all three axes. This is, according to our definition, heterogeneity.

## Slide 7
  The system benefits of storage capabilities
3. Context and research questions
Services that can be provided by EES technologies. Source: (Fitzgerald et al., 2015)
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 8
1. Context and research questions
Would investments in storage capacity be cost-optimal on these settings?
Remark 1: Cost-optimality assumes a system perspective assessment with an unique solution.
What is the system value added by storage?
Remark 2: In such framework the value corresponds to the net social value.
What are the distributional effects of such investments?
Remark 3: What is in stake is the surplus variations across market players triggered by optimal storage
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Remark1: which don’t necessarily correspond to private/project profitability due absence of markets and/or regulatory veils.

## Slide 9
  Welfare effects of storage:
2. Definitions and methodology for valuating flexibility technologies
MPC: marginal production cost
MCB: marginal consumer benefit
Mid and long-term (capital stock re-allocations):
Generation and flexibility investments are co-optimized, meaning that the slope and the rotation extent of the MPC curve is adjusted to enhance technologic complementarities, which makes the social welfare gains to be maximized.
Short-term:
Welfare effect of storage during peak and off-peak periods. Source: (Grünewald, 2011)
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 10
Interrelated and system dependent issues
Long-term
(years)
  Capacity adequacy problems
  Energy security issues
  Scissor effect
Short-term
(h)
  Missing money problem
  Merit Order Effect
  Higher operational cost for committed units
  Less flexible dispatch but higher flexibility is needed
Real time
(sec-min)
  Balancing issues
  Congestion management difficulties
  Increased need for ancillary services
Capital allocation
Economic-dispatch
Reliability requirements
2. Definitions and methodology for valuating flexibility technologies
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Intercorrelated effects, need for an holistic approach => System study

## Slide 11
S.T. operational constraints:
Ramping constraints
Min/max generation level
Part load efficiencies
FRR requirements
DSM and EES operating constraints
Capacity obligation (CRM)
Clean energy policies…
min
System cost represented as:
LT
RT
Set | Element | Description
T | ,tt T | Time slice
I | I I | Generation technologies
I Con | I | Conventional technologies
I VRE | I | Renewable energy sources
I EES | I | Electric energy storage technologies
DSM LC | DSM | Demand side management for load curtailment
DSM LS | DSM | Demand side management for load shifting
Set | Element | Description
T |  | Time slice
I |  | Generation technologies
 |  | Conventional technologies
 |  | Renewable energy sources
 |  | Electric energy storage technologies
 |  | Demand side management for load curtailment
 |  | Demand side management for load shifting
2. Definitions and methodology for valuating flexibility technologies
ST
(optional)
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Operation research problem
DIFLEXO: Dispatch, investments and flexibility optimization model
A self-developed tool for market design benchmarking and technology valuation

## Slide 12
2. Definitions and methodology for valuating flexibility technologies
Experimental setup:
Brownfield optimization considering existing
capacities on 2015.
DIFLEXO formulation: EOM, FRR and CRM and VoLL (perfect foresight)
Peak load = 93.63 GW
Total energy =541.4 TWh/year
VoLL = 10 000 €/MWh
Annual Lost load < 3 h/year
Bulk storage technologies (EES) : PHS, DCAES, ACAES, VRFB, NaS, Li-ion
DSM: Load curtailment and load shifting less than 1% and 2% of load respectively
 |  | Horizon 2020 | Horizon 2030
VRE shares | > | 27% | 40%
Nuclear shares | < | Current levels of 2015 | 50%
CO2 cost [€/ton] | = | 20 | 20
Cost assumptions | appendix | JRC-ETRI projections for 2020 | JRC-ETRI projections for 2030
Solved in GAMS under CPLEX 12.5 using the barrier algorithm
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Installed capacity

## Slide 13
3. Findings for the case of France
Technology | Investments | Retirements | Total capacity H2020
 | [GW] | [GW] | [GW]
Nuclear | - | - | 63,13
Hard coal | - | -6,34 | -
CCGT | - | -10,46 | -
OCOT | 15,87 | - | 15,87
OCGT | - | - | 8,78
Reservoir | - | - | 8,21
Wind | 44,38 | - | 51,36
PV | - | - | 3,43
PHS | - | - | 4,30
DSM | 4,68 | - | 4,68
By 2020:
No EES capacity is cost-optimal => storage adds no value
Min. | 1st Qu. | Median | Mean | 3rd Qu. | Max.
[€/MWh] | [€/MWh] | [€/MWh] | [€/MWh] | [€/MWh] | [€/MWh]
-27,0 | 31,7 | 37,4 | 32,5 | 42,2 | 92,3
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 14
3. Findings for the case of France
However, by 2030 some EES investments are cost-optimal:
Technology | Investments |  | Retirements |  | Total capacity | 
 | [GW] |  | [GW] |  | [GW] | 
 | EES | noEES | EES | noEES | EES | noEES
Nuclear | - | - | -14,04 | -15,11 | 49,09 | 48,02
Hard coal | - | - | -4,06 | -4,63 | 2,28 | 1,71
CCGT | - | - | - | - | 10,46 | 10,46
OCOT | 8,61 | 11,72 | - | - | 8,61 | 11,72
OCGT | - | - | - | - | 8,78 | 8,78
Reservoir | - | - | - | - | 8,21 | 8,21
Wind | 72,73 | 73,28 | - | - | 79,71 | 80,26
PV | 16,62 | 19,90 | - | - | 20,05 | 23,33
PHS | - | - | - | - | 4,30 | 4,30
DSM | 4,68 | 4,68 | - | - | 4,68 | 4,68
DCAES | 2,00 | - | - | - | 2,00 | -
ACAES2 | 1,23 | - | - | - | 1,23 | -
v
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
v
v

## Slide 15
3. Findings for the case of France
Click to see the hourly dispatch
Results: The supply curve changes as well as the dispatch schedules
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Two different mixes… => Changes in the supply curve and in the optimal dispatch

## Slide 16
3. The public value of electricity storage and its welfare effects
There surplus variations of consumers are due to electricity price variations:
 | Min. | 1st Qu. | Median | Mean | 3rd Qu. | Max.
 | [€/MWh] | [€/MWh] | [€/MWh] | [€/MWh] | [€/MWh] | [€/MWh]
EES | -17,3 | -8,5 | 98,1 | 68,1 | 106,1 | 158,7
noEES | -19,4 | -19,4 | 100,1 | 65,5 | 108,7 | 172,4
 | Price of Capacity obligations | RPS | Nuclear cap
 | [€/MW.year] | [€/MWh] | [€/MWh]
EES | 29 649 | 7,46 | 68,76
noEES | 44 962 | 12,92 | 65,76
Electricity price statistics
Other markets (Marginals)
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 17
3. Findings for the case of France
The value of storage by H2030
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 18
3. Findings for the case of France
Welfare effects of storage by H2030
The net surplus variation is 670 M€/year, which is around 2.7% of total system cost
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: The surplus variation of consumers, VRE and ACAES is positive, while producers are worst-off.

## Slide 19
4. Conclusions
A clear definition and a convenient methodology has been applied for assessing the value of new flexibility technologies.
An integrated valuation approach based on the DIFLEXO model has been implemented to study the case of France:
  H2020: even if there is a higher need for flexibility, storage investments are not cost optimal.
  H2030: CAES technologies are cost-optimal provided that:
    They participate on VRE integration, supply FRR services and participating on capacity adequacy with no regulatory veils.
    The system value of cost-optimal storage is around 350 m €/year which is 1.3% of total system cost.
    Important distributional effects appear. This is due to the reduction of revenues coming from the CRM and FRR markets. Nevertheless, VRE producers and consumers are better-off.
Effective CO2 price signals is required for storage to contribute to emission reduction targets: EES shows complementarities with low run marginal cost technologies, enhancing its market shares. In the absence of effectively pricing environmental externalities, EES can increase CO2 emissions.
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 20
REFERENCES
Carlsson, Johan et al. “Energy Technology Reference Indicator Projections for 2010-2050.” Luxembourg, 2014. doi:10.2790/057687.
Fitzgerald, Garrett, James Mandel, Jesse Morris, and Touati Hervé. “The Economics of Battery Energy Storage: How Multi-Use, Customer-Sited Batteries Deliver the Most Services and Value to Customers and the Grid,” 2015.
Grünewald, Philipp. “The Welfare Impact of Demand Elasticity and Storage,” no. September (2011): 1–5.
Hentschel, Julia, Ugljesa Babic, and Hartmut Spliethoff. “A Parametric Approach for the Valuation of Power Plant Flexibility Options.” Energy Reports 2 (2016): 40–47. doi:10.1016/j.egyr.2016.03.002.
Hirth, Lion, Falko Ueckerdt, and Ottmar Edenhofer. “Integration Costs Revisited - An Economic Framework for Wind and Solar Variability.” Renewable Energy 74 (2015): 925–39. doi:10.1016/j.renene.2014.08.065.
Kumar, N, P Besuner, S Lefton, D Agan, and D Hilleman. “Power Plant Cycling Costs Power Plant Cycling Costs.” 15013 Denver West Parkway Golden, Colorado 80401 303-275-3000, 2012.
Scitovsky, Tibor. “Two Concepts of External Economies.” The Journal of Political Economy 62, no. 2 (1954): 143–51. doi:10.1086/257498.
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 21
manuel.villavicenio@dauphine.com
http://www.ceem-dauphine.org/working/en/THE-VALUE-OF-ELECTRIC-ENERGY-STORAGE-IN-ELECTRICITY-SYSTEMS-WITH-HIGH-SHARES-OF-WIND-AND-SOLAR-PV
Working paper available at:
“What is a cynic? A man who knows the price of everything and the value of nothing”
Oscar Wilde

## Slide 23
3. The public value of electricity storage and its welfare effects
Benefits
Value
Monetizable benefits
Markets
EOM, FRR, CRM
Defining the meaning of “value”:
“The value of storage is defined as the monetizable system benefits generated directly or indirectly by storage, provided a cost-optimized system including capacity allocations, as well as dispatch and inventory decisions.”
Vs.
“Cost based analyses” consider technologies in isolation
(e.g., LCOE, LCOS)
“Value based analyses” consider interactions between technologies
(e.g., partial equilibrium setting)
Experimental Setup using DIFLEXO
Optimizing the system with and w/o EES technologies
The value sources correspond to the costs categories considered in the objective function.
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 24
3. The public value of electricity storage and its welfare effects
Costs and revenues for producers
System operations
Market revenues
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University
Notes: Total costs presented by technology
Revenues introduces assuming marginal pricing markets..

## Slide 25
3. The public value of electricity storage and its welfare effects
12.33 bn€
13.38 bn€
Surplus variations of producers due to market share and price variations. Producers profits are positives in both cases but are higher in the reference case without storage.
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 26
3. The public value of electricity storage and its welfare effects
Accumulated cost
Results: Costs variations
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University

## Slide 27
Accumulated revenue
3. The public value of electricity storage and its welfare effects
Manuel Villavicencio. Université Paris-Dauphine, PSL Research University