## Slide 1: Impact of storage efficiency and charging costs on storage profitability in the electricity market 15th IAEE European Conference 2017 Vienna – 6th September 2017
Andreas Belderbos
Erik Delarue
Kris Kessels
William D’haeseleer

## Slide 2: Overview
The Levelized Cost of Electricity – LCOE
The Levelized Cost of Storage – LCOS
Insights in storage cost metrics
Shortcomings of metrics
Using storage cost metrics

## Slide 3: Levelized Cost of Electricity - LCOE
The LCOE is defined as the fictitious average electricity price during its operation hours and needed over the lifetime of the plant to break even the full costs for the investor (including the desired rate of return which is included in the discount rate r).
Average electricity price during generation
OCC
OM
Fuel
CO2
D
€/MWh
Overnight Capital Cost
Decommissioning
Operating & maintenance

## Slide 4: Levelized Cost of Storage - LCOS
The LCOS is defined as the fictitious average electricity price during its discharging hours and needed over the lifetime of the plant to break even the full costs for the investor (including the desired rate of return which is included in the discount rate r).
Average electricity price during discharging
€/MWh
Total Charging Cost
OCC
Fixed OM
Average Charging cost per MWhd
Efficiency losses
Charging cost of useful electricity
= Average Charging cost per MWhc = €/MWhc

## Slide 5: Additional metrics
Since ‘primary energy’ is same commodity as ‘secondary energy’
Required Average Discharge Price – RADP ( = LCOS)
Required Average Price Spread – RAPS
Required Average Operational Profit – RAOP
Average electricity price during discharging
€/MWh
OCC
Fixed OM
Efficiency losses
Average charging cost per MWhc
Efficiency losses
OCC
Fixed OM
OCC
Fixed OM
RADP
RAPS
RAOP
Average charging cost per MWhc
Average charging cost per MWhd

## Slide 6: Key parameters
Capital cost
O&M
Charging cost
MWh discharged
Total Charging Cost
Average charging price per MWhc
Efficiency
Overnight Construction Cost

## Slide 7: Storage parameters used for illustration
Installed power capacity (P) | 1 MW
Equivalent Annual Fixed cost (OCC + FOM) | 30,000 €
Round-trip efficiency (ηRT) | 80 %
Number of discharging hours (NDH) | 1000 h
Averaged charging cost (ACC) | 20 €/MWhc

## Slide 8: Varying the average charging price
RADP
RAPS
RAOP
Notes: If ACC = 0, all metrics equal !This effectively means that even for the RADP and RAPS, no efficiency is taken into account.

## Slide 9: Varying the round-trip efficiency
RADP
RAPS
RAOP

## Slide 10: Using the different cost metrics
Levelized cost metrics work well when unit is fully dispatchable
-> storage is dispatchable…
… unless the energy capacity is limited
Occurring price profile <-> available price profile

## Slide 11: Correctly using the different cost metrics
RADP
AADP
Compare the required cost metrics to the corresponding available price metric
RAPS
AAPS
RAOP
AAOP
Required prices
Available prices

## Slide 12: Caution with the charging cost
If assumed charging cost differs from actual available charging cost, intersection is not necessarily the break-even point
Required prices
Available price
Required Average Operational Profit -> Most transparent metric

## Slide 13: Analyzing the Required Average Operational Profit for different price profiles
AAOP for multiple years
RAOP

## Slide 14: Wrap-up
LCOE
For charging cost = 0 €/MWh: RADP = RAPS = RAOP: neglecting efficiency
Caution when using metrics for storage with limited energy capacity
RAOP is most transparent metric and preferred
Required Average Discharge Price (RADP)
Required Average Price Spread (RAPS)
Required Average Operational Profit (RAOP)

## Slide 15: Reference & Contact
Contact: andreas.belderbos@kuleuven.be
KU Leuven – TME
Energy & Environment
Paper available:
A. Belderbos, E. Delarue, K. Kessels, W. D'haeseleer,
Levelized cost of storage — Introducing novel metrics,
Energy Economics, Available online 1 September 2017