## Slide 1: Financial Feasibility of Storage Technologies in Electricity Systems
Empirical Evidence from Chile
Héctor Osorio, Carlos Silva, Shahriyar Nasirov, and Claudio A. Agostini
Universidad Adolfo Ibañez
IAEE 2017
Vienna, Austria, 03-06 September 2017
Session 6G
Wednesday, September 06, 11:00 am – 12:30 am

## Slide 2: Presentation overview
Introduction
Methodology
Results
Conclusion

## Slide 3: Chilean electric market
Market of financial bilateral contracts
G1
G3
G2
Spot Market
Distributor
Regulated client
Free client 1
Free client 2
Free client 3
Purchase/sale to spot market
Regulated contract
Contract by direct negotiation

## Slide 4: Evolution of Chilean Energy Matrix
Source: Solar Energy Research Center. 2016

## Slide 5: Renewables and it challenges
RPS scheme (Renewable Portfolio Standards) – 20% renewable energy target by 20251
Favorable solar radiation
Challenges
Reliability of supply
Variability of supply
Generation disconnected from demand
Oversized transmission systems
Frequency
Voltage
1: Installed capacity of 22,000 MW approximately
Source: Generadoras Chile. 2017

## Slide 6: Energy storage systems in Chile
First energy storage system installed in 2009 (12 MW-3MWh Li-ion batteries)
Second energy storage system installed in 2011 (20 MW-5MWh Li-ion batteries)
Future projects
  Espejo de Tarapacá (300 MW hydro pump storage system)
  Cerro Dominador (110 MW CSP with 17.5 hours of energy storage)
  Are Energy Storage Systems economically feasible in Chile?

## Slide 7: Methodology
Annual benefits vs. costs
Price arbitrage
Diminishment in transmission losses
Defer of transmission investment
2: To determine annual costs, a WACC of 6,67% was calculated
Annual benefits
Different spot price for each hour
Less transmission losses
Annual costs
Annuity of investment2
O&M costs

## Slide 8: Methodology

## Slide 9: Methodology
Defer of transmission investment
Chart: Hours
No storage | 0 | 0 | 0 | 0 | 0 | 0 | 0.1028 | 30.1341 | 138.7795 | 187.5793 | 194.9042 | 194.6842 | 196.0202 | 197.8496 | 198.7758 | 199.1974 | 194.2332 | 161.3823 | 109.6586 | 26.2194 | 0.2809 | 0 | 0 | 0
Storage | 0 | 0 | 0 | 0 | 0 | 0 | 0.1028 | 30.1341 | 138.7795 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 135.579 | 0 | 0 | 0
Chart: Hours
Storage | 69.178 | 0 | 0 | 0 | 0 | 0 | 0.137 | 40.1789 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150
No storage | 0 | 0 | 0 | 0 | 0 | 0 | 0.137 | 40.1789 | 185.0393 | 250.1058 | 259.8723 | 259.5789 | 261.3603 | 263.7995 | 265.0344 | 265.5966 | 258.9776 | 215.1764 | 146.2114 | 34.9592 | 0.3745 | 0 | 0 | 0
Solar Jama 50% capacity increase
Solar Jama 100% capacity increase
Source: Obtained from simulations
Source: Obtained from simulations

## Slide 10: Results: Price arbitrage
Chart: Hours
Andes Solar | 84.0383 | 78.1312 | 73.7218 | 70.5913 | 69.5972 | 67.5514 | 66.78 | 63.9495 | 53.257 | 47.6359 | 47.2546 | 47.9027 | 46.5324 | 43.4645 | 42.031 | 42.4197 | 44.3224 | 51.3105 | 61.1613 | 71.7062 | 80.9957 | 88.7191 | 90.6635 | 87.6941
Finis Terrae | 81.9424 | 76.182 | 71.8833 | 68.8304 | 67.8682 | 65.8623 | 65.1077 | 62.3512 | 51.9233 | 46.4627 | 46.0868 | 46.7265 | 45.4011 | 42.4144 | 41.0254 | 41.4027 | 43.2525 | 50.0198 | 59.6026 | 69.9045 | 79.0051 | 86.5555 | 88.466 | 85.5416
La Huayca II | 85.4525 | 79.4162 | 74.9286 | 71.7374 | 70.7383 | 68.6437 | 67.8466 | 64.9839 | 54.1368 | 48.4167 | 48.0102 | 48.6854 | 47.3091 | 44.2003 | 42.7457 | 43.1388 | 45.0677 | 52.1801 | 62.2366 | 73.0147 | 82.45 | 90.2902 | 92.275 | 89.2206
María Elena | 83.1143 | 77.2987 | 73.2549 | 70.4624 | 69.3975 | 67.13 | 66.5377 | 63.6421 | 52.9556 | 47.2774 | 46.6943 | 47.2039 | 45.8355 | 42.8209 | 41.3639 | 41.728 | 43.8242 | 50.8777 | 60.8069 | 71.5118 | 80.9806 | 88.8056 | 90.683 | 87.6563
Solar Jama | 82.4368 | 76.2715 | 71.692 | 69.8161 | 69.1185 | 66.9777 | 67.5833 | 65.2445 | 52.9942 | 49.6064 | 49.1416 | 49.5618 | 46.8526 | 43.9997 | 42.6153 | 43.9793 | 45.5964 | 52.2188 | 61.997 | 72.2801 | 80.4534 | 86.0986 | 88.1318 | 84.867
Valle los Vientos | 0 | 0
Source: Obtained from simulations
Source: CDEC – SING 2016

## Slide 11: Results: Diminishment in transmission losses
Chart: Hours
María Elena | 0 | 0 | 0 | 0 | 0 | 0 | 0.0028123 | 3.9487 | 29.0759 | 50.2176 | 53.7763 | 53.8707 | 53.4407 | 53.4481 | 53.2617 | 53.1095 | 51.0838 | 38.195 | 26.1547 | 5.7201 | 0.079097 | 0 | 0 | 0
Valle los Vientos | 5.1119 | 6.5729 | 8.4354 | 10.1063 | 11.5194 | 12.8105 | 14.1483 | 15.0866 | 15.1185 | 10.1873 | 4.4565 | 4.4613 | 16.455 | 41.0957 | 60.6375 | 68.8354 | 71.4165 | 69.6855 | 64.4963 | 55.0431 | 40.6952 | 24.3171 | 10.2707 | 4.7555
Chart: Hours
Andes Solar | 84.0383 | 78.1312 | 73.7218 | 70.5913 | 69.5972 | 67.5514 | 66.78 | 63.9495 | 53.257 | 47.6359 | 47.2546 | 47.9027 | 46.5324 | 43.4645 | 42.031 | 42.4197 | 44.3224 | 51.3105 | 61.1613 | 71.7062 | 80.9957 | 88.7191 | 90.6635 | 87.6941
Finis Terrae | 81.9424 | 76.182 | 71.8833 | 68.8304 | 67.8682 | 65.8623 | 65.1077 | 62.3512 | 51.9233 | 46.4627 | 46.0868 | 46.7265 | 45.4011 | 42.4144 | 41.0254 | 41.4027 | 43.2525 | 50.0198 | 59.6026 | 69.9045 | 79.0051 | 86.5555 | 88.466 | 85.5416
La Huayca II | 85.4525 | 79.4162 | 74.9286 | 71.7374 | 70.7383 | 68.6437 | 67.8466 | 64.9839 | 54.1368 | 48.4167 | 48.0102 | 48.6854 | 47.3091 | 44.2003 | 42.7457 | 43.1388 | 45.0677 | 52.1801 | 62.2366 | 73.0147 | 82.45 | 90.2902 | 92.275 | 89.2206
María Elena | 83.1143 | 77.2987 | 73.2549 | 70.4624 | 69.3975 | 67.13 | 66.5377 | 63.6421 | 52.9556 | 47.2774 | 46.6943 | 47.2039 | 45.8355 | 42.8209 | 41.3639 | 41.728 | 43.8242 | 50.8777 | 60.8069 | 71.5118 | 80.9806 | 88.8056 | 90.683 | 87.6563
Solar Jama | 82.4368 | 76.2715 | 71.692 | 69.8161 | 69.1185 | 66.9777 | 67.5833 | 65.2445 | 52.9942 | 49.6064 | 49.1416 | 49.5618 | 46.8526 | 43.9997 | 42.6153 | 43.9793 | 45.5964 | 52.2188 | 61.997 | 72.2801 | 80.4534 | 86.0986 | 88.1318 | 84.867
Valle los Vientos | 0 | 0
Source: CDEC – SING 2016
Source: CDEC – SING 2016
Source: Obtained from simulations

## Slide 12: Results: Defer of transmission investment
Chart: Hours
Andes Solar | 84.0383 | 78.1312 | 73.7218 | 70.5913 | 69.5972 | 67.5514 | 66.78 | 63.9495 | 53.257 | 47.6359 | 47.2546 | 47.9027 | 46.5324 | 43.4645 | 42.031 | 42.4197 | 44.3224 | 51.3105 | 61.1613 | 71.7062 | 80.9957 | 88.7191 | 90.6635 | 87.6941
Finis Terrae | 81.9424 | 76.182 | 71.8833 | 68.8304 | 67.8682 | 65.8623 | 65.1077 | 62.3512 | 51.9233 | 46.4627 | 46.0868 | 46.7265 | 45.4011 | 42.4144 | 41.0254 | 41.4027 | 43.2525 | 50.0198 | 59.6026 | 69.9045 | 79.0051 | 86.5555 | 88.466 | 85.5416
La Huayca II | 85.4525 | 79.4162 | 74.9286 | 71.7374 | 70.7383 | 68.6437 | 67.8466 | 64.9839 | 54.1368 | 48.4167 | 48.0102 | 48.6854 | 47.3091 | 44.2003 | 42.7457 | 43.1388 | 45.0677 | 52.1801 | 62.2366 | 73.0147 | 82.45 | 90.2902 | 92.275 | 89.2206
María Elena | 83.1143 | 77.2987 | 73.2549 | 70.4624 | 69.3975 | 67.13 | 66.5377 | 63.6421 | 52.9556 | 47.2774 | 46.6943 | 47.2039 | 45.8355 | 42.8209 | 41.3639 | 41.728 | 43.8242 | 50.8777 | 60.8069 | 71.5118 | 80.9806 | 88.8056 | 90.683 | 87.6563
Solar Jama | 82.4368 | 76.2715 | 71.692 | 69.8161 | 69.1185 | 66.9777 | 67.5833 | 65.2445 | 52.9942 | 49.6064 | 49.1416 | 49.5618 | 46.8526 | 43.9997 | 42.6153 | 43.9793 | 45.5964 | 52.2188 | 61.997 | 72.2801 | 80.4534 | 86.0986 | 88.1318 | 84.867
Valle los Vientos | 0 | 0
Source: Obtained from simulations
Chart: Hours
No storage | 0 | 0 | 0 | 0 | 0 | 0 | 0.1028 | 30.1341 | 138.7795 | 187.5793 | 194.9042 | 194.6842 | 196.0202 | 197.8496 | 198.7758 | 199.1974 | 194.2332 | 161.3823 | 109.6586 | 26.2194 | 0.2809 | 0 | 0 | 0
Storage | 0 | 0 | 0 | 0 | 0 | 0 | 0.1028 | 30.1341 | 138.7795 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 135.579 | 0 | 0 | 0
Source: CDEC – SING 2016
Source: CDEC – SING 2016

## Slide 13: Conclusion
Energy storage is needed to connect supply and demand of renewables
Energy storage is technically capable, but expensive
Price arbitrage seems to be the best option
Government subsidies needed
Not recommended until price drops to around a third or the obtainable benefits increase